## Slide 1: Vivo Active 2D Touch Surface
04-29-2020
Andy Appeldorn

## Slide 2: Demo Construction
Disassembled Garmin vívoactive® 4
  Housing, Touch Sensor, Li-Ion Battery
Main PCB
  SAML10 MCU for 2D cap touch
  RN4678 for wireless comm to 2D GUI
    BT 2.0 SPP Profile
  USB Li-Ion Battery Charger IC
  USB-CDC Comm for wired testing

## Slide 3: Software Configuration

## Slide 4: Hardware Overview
SAML10 Features
  Core
    Arm Cortex-M23 Core
    32MHz (2.62 CoreMark/MHz and up to 31 DMIPS)
    1.62-3.63V Operating Voltage
  Memory
    64/32/16KB Flash, 16/8/4KB SRAM, 2KB Data Flash
  WLCSP Package Details
    32 pin, 25 I/Os
    .4mm lead pitch
    2.79x2.79x.482 mm

## Slide 5: Hardware Overview
Low Power Features
  Active, Idle, Standby with partial or full SRAM retention and off standby modes
    Active mode (< 25 μA/MHz)
    Idle mode (< 10 μA/MHz) with 1.5 μs wake-up time
    Standby with Full SRAM Retention (0.5 μA) with 5.3 μs wake-up time
    Off mode (< 100 nA)
Sleepwalking peripherals
Embedded Buck/LDO regulator with on-the-fly selection

## Slide 6: Hardware Overview
PTC Touch Controller
  Up to 20 self, 100 mutual channels
  Hardware noise filtering
  Driven Shield Plus for moisture tolerance and noise immunity
  Parallel Acquisition through Polarity control
  Supports wake-up on touch from standby mode

## Slide 7: 2D Touch Surface
Self Cap acquisition
5x5 2D Touch Sensor from Vivo Active 4

## Slide 8: Outline
Hardware overview
  Presentation discussion
  Ground plane simulating display capacitive loading
2D Touch Surface GUI Intro
USB Connected Operation
Battery Operation
Wet Operation
  5% salt water solution, ½ TSP / 2 oz water
  Powered by Li-Ion, data by BT
  Bezel touch effect
Low Power and Acquisition Timing
  Different power modes
  Power Debugger Live w/ Acquisition Scope

## Slide 9: Hardware Overview
Presentation
Ground plane simulating display capacitive loading

## Slide 10: 2D Touch Surface GUI Intro
Used to visualize cap touch data in the system
Demo will be relying on:
Touch Visualization Pane
  Sensor signal levels
    Noise
    Touch Sensitivity
  Touch coordinate detected
Gesture Pane
  Gesture detected by touch controller
  Not decoded in GUI

## Slide 11: USB Connected Operation
Powered by USB, data by BT
Noise and signal
Draw horizontal, vertical, and diagonal lines
  Slow and fast
Draw gestures
  Single finger tap, swipe, wheel
  Tow finger tap, swipe, pinch zoon
Bezel touch effect
  Could be rejected by implementing palm rejection method, but may lose two finger operation due to sensor size

## Slide 12: Battery Operation (Floating GND)
Powered by Li-Ion battery, data by BT
Noise and signal
Draw horizontal, vertical, and diagonal lines
  Slow and fast
Draw gestures
  Single finger tap, swipe, wheel
  Tow finger tap, swipe, pinch zoon
Bezel touch effect
  Could be rejected by implementing palm rejection method, but may lose two finger operation due to sensor size

## Slide 13: Wet Operation
Testing using 5% saltwater solution, ½ TSP per 2 oz water
Powered by Li-Ion, data by BT
Water signal
Noise and signal
Draw horizontal, vertical, and diagonal lines
  Slow and fast
Draw gestures
  Single finger tap, swipe, wheel
  Tow finger tap, swipe, pinch zoon
Bezel touch effect
  Could be rejected by implementing palm rejection method, but may lose two finger operation due to sensor size

## Slide 14: Low Power and Acquisition Timing
Presentation discussing different power modes
Power Debugger Live w/ Acquisition Scope

## Slide 15: SAML10 Touch Surface Low Power
CPU
  16MHz internal oscillator, no DFLL
  32KHz internal oscillator
  3.3Vdc
  Buck regulator during active, LPVREG in sleep
Active w/ 16MHz internal oscillator = 415uA avg
Sleep w/ 32mS auto-scan = 29uA avg
Adjustable inactivity timeout to enter low power standby mode
Adjustable touch drift period for environmental recalibration

## Slide 16: Touch Surface Standby Operation
Active Mode
Touch Timeout Event
Standby Auto-scan
Drift Calibration

## Slide 17: Standby Auto-scan Power Comparison
Auto scan trigger period while in standby
QTM_AUTOSCAN_TRIGGER_PERIOD
Range: 8ms – 1024ms
@3.3Vdc
Chart: QTM_AUTOSCAN_TRIGGER_PERIOD (ms)
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
 | 86 | 54 | 32.5 | 23.7 | 19 | 17 | 16 | 15.3

## Slide 18: Drift Recalibration Power Comparison
Drift measurement period to wake and recalibrate reference values
DEF_TOUCH_DRIFT_PERIOD_MS
Range: 1 – 65535
32mS auto-scan rate
@3.3Vdc
Chart: DEF_TOUCH_DRIFT_PERIOD_MS (ms)
| 1000 | 2000 | 4000 | 8000 | 16000 | 32000
 | 36 | 32.7 | 30.7 | 29.7 | 29.12 | 28.91